Creating Metrology Reports using the MET/CAL or MET/TRACK Database and Access 2.0

Application Information

Occasionally, it may necessary to write a report that will get data from both Mtrack.db and Access 2.0 MDB data table.  This application note explains how to do this.

Configuring ODBC for Access

You must first configure the ODBC Administrator to allow access to the MDB data table.  To do this, open the ODBC Administrator and select MS Access 2.0 Databases (Microsoft Access Driver (*.MDB)) in the Data Sources windows.  Click Setup.  Note that this procedure will only work with the Access 2.0 in 16 bit.

And select your Access Database.  If the MS Access 2.0 Database driver is not loaded, you have to select ADD and add the MS Access 2.0 driver.

Configuring Crystal Reports

Open Crystal Reports and Select New | Custom | ODBC/SQL.

Select ODBC - MS Access 2.0 then OK.

When the Choose SQL Table window opens, click on Choose Database File then select your *.MDB database.

Add your database fields to the Details section.

Adding the Mtrack.db

Now select Database | Add Database to Report.  The ODBC Table window opens.  Select Log On Server | ODBC - Calibration Database and log onto the database.  In the SQL Database window, highlight Fluke(Calibration Database).

and select the MET table you want.   The Linking Expert opens.  You must link from your Access table to a field in the table you selected.

You may now select the fields you want from the table.

Be careful here, as a  data field in the access table must also have similar data in the table you selected.  In the above example the SupplierName is matched with I4202 (Mfg).

Your report will now have the data from both database tables.

PO Box 9090, Everett, WA USA 98206

Fluke Europe B.V.

PO Box 1186, 5602 BD

Eindhoven, The Netherlands

For more information call:

In the U.S.A. (800) 443-5853 or

Fax (425) 356-5116

In Europe (21 40) 2 678 200 or

Fax (21 40) 2 678 222

In Canada (905) 890-7600 or

Fax (905) 890-6866

From other Countries (425) 356-5500