Cables and Adapters for MET/CAL and 5500A/CAL Serial Connections

| Model Number | COM 1, COM 2, COM 3, COM 4 | COM5500/COM5520 | COM5800/COM5820] |
| --- | --- | --- | --- |

Fluke 2620A, 2625A, 2635A Hydra

Fluke 2640A, 2641A NetDAQ

| Fluke 2645A, 2646A NetDAQ | DB-9 female to DB-9 female null modem cable, Fluke PM 8914/001 CombiScope Serial Interface Cable or equivalent. | DB-9 male to DB-9 female straight cable, Fluke Part #943738 or equivalent. | DB-9 male to DB-9 female straight cable, Fluke Part #943738 or equivalent. |
| --- | --- | --- | --- |
| Fluke 39, 40, 41 | No closed loop procedure available. | No closed loop procedure available. | No closed loop procedure available. |
| Fluke 45 | DB-9 female to DB-9 female null modem cable, Fluke PM 8914/001 CombiScope Serial Interface Cable or equivalent. | DB-9 male to DB-9 female straight cable, Fluke Part #943738 or equivalent. | DB-9 male to DB-9 female straight cable, Fluke Part #943738 or equivalent. |

Fluke 5500A, 5520A

| Fluke 5800A, 5820A | DB-9 female to DB-9 female null modem cable, Fluke PM 8914/001 CombiScope Serial Interface Cable or equivalent. | n/a | n/a |
| --- | --- | --- | --- |

Fluke 93, 95, 97, 97/AUTO

Fluke 91, 92, 96, 99

| Fluke 105 | Fluke PM 9080 Optical Interface Cable. | Fluke PM 9080 Optical Interface Cable. DB-9 male to DB-9 male null modem adapter, Fluke Adapter Kit #689486 or equivalent.. | Fluke PM 9080 Optical Interface Cable. DB-9 male to DB-9 male null modem adapter, Fluke Adapter Kit #689486 or equivalent. |
| --- | --- | --- | --- |
| Fluke 701 | Fluke Service Cable, part #949446, or equivalent. | Not supported. | Not supported. |
| Fluke 702 | DB-9 male to DB-9 female straight cable, Fluke Part #943738 or equivalent. | Not supported. | Not supported. |
| Fluke 725 | Fluke Service Cable, part #949446, or equivalent. | Fluke Service Cable, part #949446, or equivalent. DB-9 male to DB-9 male null modem adapter, Fluke Adapter Kit #689486 or equivalent | n/a |
| Fluke 744 | Fluke Service Cable, part #949446, or equivalent. | Not supported. | Not supported. |
| Fluke 787 | See instructions in the Fluke 787 Service Manual. | Not supported. | Not supported. |
| Fluke 863, 865, 867 | Fluke PM 9080 Optical Interface Cable. | Fluke PM 9080 Optical Interface Cable. DB-9 male to DB-9 male null modem adapter, Fluke Adapter Kit #689486 or equivalent.. | n/a |
| Fluke 87, 89 Series IV | JETEYE PC IR Adapter, Fluke part #690518. DB-9 IR Cable Adapter Connector, Fluke part #8045549. | JETEYE PC IR Adapter, Fluke part #690518, DB-9 IR Cable Adapter Connector, Fluke part #8045549 and DB-9 male to DB-9 male null modem adapter, Fluke Adapter Kit #689486 or equivalent. | n/a |

Fluke PM 3082, PM 3084, PM 3092, PM 3094

Fluke PM 3335, PM 3337, PM 3350A, PM 3352A

| Fluke PM 3365A, PM 3367A, PM 3370A, PM 3375, PM 3377 | DB-9 female to DB-9 female null modem cable, Fluke PM 8914/001 CombiScope Serial Interface Cable or equivalent. | DB-9 male to DB-9 female straight cable, Fluke Part #943738 or equivalent. | DB-9 male to DB-9 female straight cable, Fluke Part #943738 or equivalent. |
| --- | --- | --- | --- |

Fluke PM 3380, PM 3382, PM 3382A, PM 3384, PM 3384A, PM 3384E

| Fluke PM 3390A, PM 3392, PM 3392A, PM 3394, PM 3394A | DB-9 female to DB-9 female null modem cable, Fluke PM 8914/001 CombiScope Serial Interface Cable or equivalent. | DB-9 male to DB-9 female straight cable, Fluke Part #943738 or equivalent. | DB-9 male to DB-9 female straight cable, Fluke Part #943738 or equivalent. |
| --- | --- | --- | --- |
| HP3325B |
|  | HP 34401A, 34420A | DB-9 female to DB-9 female null modem cable, Fluke PM 8914/001 CombiScope Serial Interface Cable or equivalent. | Not supported. The instruments uses DTR/DSR hardware handshaking, which is not supported by the 5500A UUT port. (The 5500 UUT port supports RTS/CTS hardware handshaking, XON/XOFF handshaking, or no handshaking.) | Not supported. The instruments uses DTR/DSR hardware handshaking, which is not supported by the 5500A UUT port. (The 5500 UUT port supports RTS/CTS hardware handshaking, XON/XOFF handshaking, or no handshaking.) |
| Keithley 2000 | DB-9 male to DB-9 female straight cable, Fluke Part #943738 or equivalent. |

5500A firmware version 1.10 and earlier:  DB-9 male to DB-9 male cable with the following configuration:

pin 2 <--> pin 3

pin 3 <--> pin 2

pin 5 <--> pin 5

Pins 7 and 8 must not be connected.

5500A firmware version 1.11 and later: DB-9 male to DB-9 female straight cable, Fluke Part #943738 or equivalent. DB-9 male to DB-9 male null modem adapter, Fluke Adapter Kit #689486 or equivalent.

5500A firmware version 1.10 and earlier:  DB-9 male to DB-9 male cable with the following configuration:

pin 2 <--> pin 3

pin 3 <--> pin 2

pin 5 <--> pin 5

Pins 7 and 8 must not be connected.

| 5500A firmware version 1.11 and later: DB-9 male to DB-9 female straight cable, Fluke Part #943738 or equivalent. DB-9 male to DB-9 male null modem adapter, Fluke Adapter Kit #689486 or equivalent. |
| --- |
| Marconi 2024 | DB-9 female to DB-25 female null modem cable Fluke RS40 RS232C Terminal Cable of equivalent. | DB-9 female to DB-25 female straight cable Fluke RS41 RS232C Terminal Cable of equivalent. | DB-9 female to DB-25 female straight cable Fluke RS41 RS232C Terminal Cable of equivalent. |
| Tektronix 710, 720 TEKSCOPE | Use RS-232C Interface Cable supplied with unit. | Use RS-232C Interface Cable supplied with unit. DB-9 male to DB-9 male null modem adapter, Fluke Adapter Kit #689486 or equivalent. |
|  | Tektronix TDS Series Scopes | DB-9 female to DB-9 female null modem cable, Fluke PM 8914/001 CombiScope Serial Interface Cable or equivalent. | DB-9 male to DB-9 female straight cable, Fluke Part #943738 or equivalent. | DB-9 male to DB-9 female straight cable, Fluke Part #943738 or equivalent. |