# ******************** GET STANDARD DEVIATION ********************

# This procedure cumulatively calculates the std dev from a series

# of readings presented in MEM in units of nominal

# Set M[61],M[62],M[63],M[64] and M[65]=0 to start with

#M[61] = Sum of readings

#M[62] = Which reading is this

#M[63] = Sum of readings squared

#M[64] = Sum of square of readings

#M[65] = Holds final SD value

4.004  MATH         M[62]=M[62]+1;M[61]=MEM+M[61]

4.005  MATH         M[63]=M[61]*M[61];M[64]=(MEM^2)+M[64]

4.006  JMPL         SKIP_FIRST_READING M[62]==1

4.007  MATH         M[65]=M[64]-(M[63]/M[62])

4.008  MATH         M[65]=SQRT (ABS(M[65]/(M[62]-1)))

# Calculate SD % noise (M[66]) and SD in ppm (M[67])

4.009  MATH         M[66]=ABS((M[65]/M[49])*100)

4.010  MATH         M[67]=ABS(M[65]/(MEM + 1E-30))

4.011  LABEL        SKIP_FIRST_READING

4.013  END